## Slide 1
SMART HOME AUTOMATION
MINOR PROJECT
FACULTY ADVISOR : Dr. PHANIKRISHNA
PRESENTED BY:
SAURABH TIWARI-521234
YUVASRI G-521262

## Slide 2
Revolutionizing Your Home with Smart Automation
Let's make a Home Automation Project to control the appliances in multiple rooms of your home using INTERNET OF THINGS with a Firebase Real-time Database and ESP 32.

## Slide 3
Introduction:-
Let's make a Home Automation Project to control the multiple rooms of your home with a Firebase Real-time Database ,and ESP32. This is an IOT home automation project. We have also created an Android App using MIT App Inventor. You can use the App to control total 4 rooms of you home. You can also add more rooms in the Android App by modifying the project aia file. You can also check the real time status update by using the Android App. We have also added the manual switches to control the appliances of different rooms. If you reset the micro controller, or If there is a power failure. And when the micro controller power up again, the latest status of the relays will be updated automatically.

## Slide 4
Components Used :
ESP32 Development Board
4 Channel Relay Module (2x)
AC Bulbs (4x)
Bulb Holder (4x)
5v Power Adapter
Push Buttons (8x)
Breadboard
Jumper Wires (Male/Female)

## Slide 5
Software Used in This Project:
Arduino IDE (Version 1.8.20)
ESP8266 Board Package (Version 3.0.2)
ESP32 Board Package (Version 1.0.6)
Firebase ESP Client Library (Version 3.1.5)

## Slide 6
ESP32 Development Board
Unleash the Power
The ESP32 is a popular and versatile microcontroller development board that is widely used in IoT (Internet of Things) projects. It is part of the ESP-IDF (Espressif IoT Development Framework) ecosystem
Feature-Rich Innovation
Wireless Connectivity
Multitasking with Dual-Core Processing
Low Power Consumption
ESP32, allowing you to control and monitor your device through a web interface.

## Slide 7
The four-channel relay module contains four 5V relays and the associated switching and isolating components, which makes interfacing with a microcontroller or sensor easy with minimum components and connections. The contacts on each relay are specified for 250VAC and 30VDC and 10A in each case, as marked on the body of the relays
The four-channel relay

## Slide 8
Four-Channel Relay Module Specifications
Supply voltage – 3.75V to 6V
Trigger current – 5mA
Current when the relay is active - ~70mA (single), ~300mA (all four)
Relay maximum contact voltage – 250VAC, 30VDC
Relay maximum current – 10A

## Slide 9
Firebase ESP 32
Firebase is Google’s mobile application development platform that includes many services to manage data from IOS, Android, or web applications.
To follow this project, first, you need to set up a Firebase project and create a real-time database for that project. Then, you’ll program the ESP32 to store and read data from the database.

## Slide 10
WORKING FLOWCHART:

## Slide 11
Circuit diagram:-

## Slide 12
PROCEDURE:
Install Espressif System version 1.0.6
Install Firebase Client Library :-
Firebase Library is used to work with firebase Real time database, Cloud Firestore database. The library also supports other Arduino devices using Client interfaces.
Enter the hotspot/wifi SSID and Password.
Enter the firebase WEB API KEY.
Enter the firebase HOST URL.
Select the String room_no for the ESP device.
Select the board from the tool button and upload the code to the board

## Slide 13
After uploading the code open serial monitor.
The project will continue to the wifi router
Now the project will Signup to the firework database. As anonymous user.
Now project will fetch the latest data from the room one of the firebase database and relay database will be keep updating as per relay input

## Slide 14
PSEUDO CODE:
// Import necessary libraries
import WiFiLibrary
import FirebaseLibrary
// Define constants
const WIFI_SSID = "Yuva"
const WIFI_PASSWORD = "its me hi"
const API_KEY = "AIzaSyAwRqduc_c6tBZq8p5C-FInE3w12Oaq-4U"
const DATABASE_URL = "https://homeautomation-482f2-default-rtdb.firebaseio.com/"
const room_no = "room1"
// Define GPIO pins
const Relay1 = 13
const Relay2 = 12
const Relay3 = 14
const Relay4 = 27
const Switch1 = 23
const Switch2 = 22
const Switch3 = 21
const Switch4 = 19
const WIFI_LED = 2
// Initialize relay states
int stateRelay1 = 0
int stateRelay2 = 0
int stateRelay3 = 0
int stateRelay4 = 0
// Define Firebase objects
FirebaseData stream
FirebaseData fbdo
FirebaseAuth auth
FirebaseConfig config
// Function to handle Firebase stream callback
function streamCallback(data):
// Process Firebase stream data
// Update relay states and perform necessary actions
// Function to handle Firebase stream timeout
function streamTimeoutCallback(timeout):
// Handle stream timeout, if needed
// Function to setup the program
function setup():
// Initialize GPIO pins
// Connect to WiFi
// Initialize Firebase configuration
// Sign up or authenticate with Firebase
// Begin Firebase stream and set callbacks
// Function to handle main program logic
function loop():
// Check WiFi connection status
// Listen to switch states
// Check Firebase connection and perform actions if ready
// Handle data changes from Firebase stream
// Function to reload relay states from Firebase
function reloadRelayStates():
// Process JSON data and update relay states
// Function to listen to physical switches
function listenSwitches():
// Check state of physical switches
// Update relay states and Firebase data if switch state changes
// Function to write data to Firebase
function FirebaseWrite(URL, data):
// Write data to the specified Firebase URL
// Main program execution
setup()
loop()

## Slide 15
CONCLUSION
Transformed Living Experience
Our smart home automation project utilizes ESP32, Relay, and Firebase for global appliance control with internet-based access and a fail-safe manual option. This sophisticated solution ensures both convenience and professional-grade reliability in home automation.
Future Enhancements
We can integrate an ESP-CAM module along with
sensors to detect intruders, monitor room
temperature, and provide a WhatsApp alert in
case of a short circuit. This augmentation would
significantly enhance the security and monitoring
capabilities of our smart home automation system,
extending its functionality to encompass a broader
range of potential scenarios.